## Slide 1: The Functional Mock-up Interface Beginners’ Tutorial
Released under Attribution-ShareAlike 4.0 International License
Contributors:
Cinzia Bernardeschi, University of Pisa
Christian Bertsch, Bosch Research
Claudio Gomes, Aarhus University
Maurizio Palmieri, University of Pisa
Torsten Sommer, Dassault Systèmes
Online Materials:
https://github.com/modelica/fmi-beginners-tutorial-2024

## Slide 2: Agenda
Part 1: Introduction to FMI (40Min)
  Motivation / History
  How does FMI work?
  Tool support
  New features in FMI 3.0
Part 2: Working with (single) FMUs (45 min)
Part 3: Interacting with multiple FMUs (45 min)
Part 4: Closing Session (10 min)
Q&A

## Slide 3
Introduction to FMI
Presenter: Christian Bertsch, Bosch Research
Online Materials:
https://github.com/modelica/fmi-beginners-tutorial-2023/tree/main

## Slide 4
Motivation, Timeline

## Slide 5: Motivation
  Define a tool-independent, free-to-use standard for exchange and co-simulation of models between different simulation tools
  Provide models in a containerized form that allow for the deployment to different targets
  Decouple Know-How
    between producers and users of FMUs
    between different specialized engineers and software programmers
  Massive Re-use of modelling investment
  IP Protection possible vial black-box model exchange

## Slide 6: Timeline : Modelisar Project  Modelica Association Project FMI
FMI 1.0 (and most part of FMI 2.0) was developed in the publicly funded project Modelisar
2008-2011: MODELISAR project
2011: Release of FMI 1.0
2012: Foundation of MAP FMI in MA Members: see FMI Webpage
2013: Release of FMI 2.0  focus of this tutorial
2021: Release of FMI 3.0

## Slide 7: Versioning of FMI
FMI uses semantic versioning:
Minor releases
Can introduce new features
Backwards compatible „FMI 3.0 FMUs will be valid FMI 3.1 FMUs“
e.g. „FMI 2.0.4“
Bugfix/Maintenance releases
No new features, only bugfixes and clarifications possible
Backwards and forward compatibility
Major releases
not backwards or forward compatible changes

## Slide 8
FMI: Technical Fundamentals
“How does FMI work?”

## Slide 9: Exporting vs. Importing tool
export as Functional Mockup Unit (FMU) accordingg to the FMI Standard
develop model
FMU
import FMU
(co-) simulate model
Exporting tools
Importing tool

## Slide 10: Models in Scope
Original Scope of FMI:
Ordinary differential equations (ODEs) with events
  You need a numerical solver for their solution
Distinction between continuous and discrete variables
There is a notion of time (or more general „independent variabl2)
Extended scope:
Purely algebraic equations
Complex discrete behavior with clocks and model partitions (FMI 3.0)
A very broad scope of use cases such as
  virtual electronic control units (ECUs),
  AI models
  …

## Slide 11: Co-Simulation (CS)
Co-Simulation: (from the FMI 3.0.1 glossary)
Coupling of several simulation programs in order to compute the global behavior of a system that consists of several subsystems.
Subsystems are coupled in the sense that the behavior of each subsystem depends on the behavior of the remaining subsystems, so that the co-simulation must be computed in a step-by-step fashion.
Each simulation program is responsible for computing the behavior of a subsystem, using the outputs produced by the other simulation programs.
There can be an additional error introduced by the co-simulation, that has to be limited to an acceptable size by using a suitable co-simulation algorithms and communication pattern (e.g. step size)

## Slide 12: The FMI Standard
The FMI Standard defines the “Functional Mock-up Interface” FMI, an interface between a model and a simulation environment.
It consists of the definition of
    a C-API (application programming interface)
    an interface description (modelDescription.xml) according to a defined schema
    the definition of an exchangeable unit, an “FMU” (Functional Mock-up Unit), technically a zip file
The FMI Standard only defines the interface of a single FMU, not the co-simulation algorithm or solver for multiple FMUs!

## Slide 13: FMU – „Functional Mock-up Unit“
A model container, that can be distributed
Technically it is realized a zip File, with ending „.fmu“
Content:
  modelDescripotion.xml: meta-data with information on the model variables, interface, capabilities and to a limited extent model structure
  Model representation
    Binaries for one or multiple platforms and/or (“black box”), and/or
    Source code (e.g C-Code)
  Optionally: Resources, documentation, Icons, port definitions
  /extra information (defined in layered standards)
myModel.fmu
model.dll
modelDescription.xml

## Slide 14: FMU for Model Exchange vs. Co-Simulation (FMI 2.0)
Model Exchange (ME)
  Importing tool provides the solver.
  Properties:
  Very tight integration of model in simulation tool
  Complex interface between importing tool and model
  Importing tool must provide a suitable solver for the model
  Used e.g. for inclusion of Modelica support in non-Modelica tools (using the solver of the importing tool)
Co-Simulation (CS)
  Exporting tool provides the solver.
  Properties:
  Tight coupling of model and a suitable solver
  Simpler interface between importing tool and model
  Freedom in the selection of a co-simulation algorithm and communication timestep to reach a stable and accurate solution
  Used in most industrial applications
Tool
Solver
FMU
Model
Tool
FMU
Model
Solver

## Slide 15: Co-Simulation (CS) Interface
Communication timestep can be different from internal steps (e.g. Variable step solver)
Calling sequence CS
  Set inputs: fmi2SetXXX(...)
    Trigger calculation until next communication point: fmi2doStep(...)
    Get outputs: fmi2GetXXX(...)
For an implementation in C, see e.g. fmusim in the Reference FMUs: https://github.com/modelica/Reference-FMUs/blob/main/fmusim/fmusim_fmi2_cs.c
You can view the calling sequence with fmusim --log-fmi-calls
The co-simulation algorithm is not part of the FMI standard. It is responsible for:
  advancing the overall simulation time,
  exchange input and output data,
  triggering of input clocks, and handling events.
Internally the FMU can have different timesteps (e.g. a variable step solver)

## Slide 16: Model Exchange (ME) Interface
Main idea: the ME interface exposes the right hand side (RHS) of a hybrid ODE to the external solver.
The importer controls the data exchange and the synchronization between FMUs.
The solver algorithm itself is not part of the FMI standard. It is responsible for:
  advancing the overall simulation time,
  exchange input and output data,
  computation of continuous state variables by time integration,
  triggering of input clocks, and
  handling events.

## Slide 17: Simulation of multiple FMUs
Numerical Solver (ME) or Co-Simulation Algorithm (CS)
or
Scheduler (SE, FMI 3.0)
Not defined by FMI Standard, but by the importing tool
Functional Mock-up Interface
Exported by: Tool 1
Tool 2
Tool 3
Tool n
…
FMU
FMU
FMU
FMU

## Slide 18: The modelDescription.xml
It contains all static information about the FMU
Definition of supported interface kinds (ME, CS, SE)
Model variables
    Inputs, outputs, parameters
  Certain information on the model structure
  Example: https://github.com/modelica/Reference-FMUs/blob/main/BouncingBall/FMI2.xml
  Attributes and capability flags, such as
    “needsExecutionTool”
    …

## Slide 19: FMI for Co-simulation Tool Wrapper Variant
Co-simulation stand-alone FMU
  self-contained FMU
Co-simulation FMI Tool Wrapper
  FMU dependent on an existing tool installation
Attribute: “needsExecutionTool”

## Slide 20: FMI Tool Support
https://fmi-standard.org/tools/: FMI supported by >= 180 Tools
Exporting tools
  Modeling and simulation tools
  Model-based software creation
  Wrapping of algorithms, virtual ECUs
  …
Importing tools
  Modeling and simulation tools
  Co-simulation tools and integration platforms
  Implementations for programming and scripting languages
  ….

## Slide 21: Compatibility Information
Replaces the cross-check that helped to improve he maturity of FMI 1.0 and 2.0 supporting tools.
Information on on how FMI export and import have been tested provided by the tool vendors and linked in the tools list
Tools providing compatibility information are marked with a golden star and listed on top of the tools list https://fmi-standard.org/tools/:

## Slide 22: Licenses and licensing mechanism
The FMI standard deals with the technical part of model-exchange and co-simulation only.
There might be other legal or technical restrictions
  Exporting tools might use a licensing mechanism such as FlexNet
  Other legal obligations, e.g., w.r.t. to the distribution of FMUs might be imposed by the exporting tools.
License information can be stored in the documentation folder

## Slide 23
New features in FMI 3.0

## Slide 24: Motivation for FMI 3.0
  180+ tools support FMI now: many users now, many new use-case requests:
  Virtual Electronic Control Units (vECUs):
    FMI 2.0 works well for physics simulations: better support for vECUs is needed
  Advanced Co-Simulation
    Co-Simulation is the more popular interface type: improved co-simulation methods are needed to improve performance and accuracy
  Multi-FMU simulations are getting more common
    Events are necessary in complex control systems
    Events must be synchronized across FMUs
  New ML and AI applications
    More derivatives computations is required
vECU
Co-Sim
Events
AI
API Efficiencies

## Slide 25: FMI 3.0: New Interface Type – Scheduled Execution
FMI 2.0
Model Exchange
Co-Simulation
FMI 3.0
Model Exchange
Co-Simulation
Scheduled Execution
Scheduled Execution allows coupling several FMUs with one, external scheduler (OS)
vECU
Events
Notes: This is necessary for collaborative development of complex system controllers

## Slide 26: FMI 3.0: Main Improvements
New Application
Performance
Accuracy
    Event mode for Co-Simulation
    Intermediate variable update
    Clocks
    New variable types
    Array variables
    Terminals and icon
    FMI for Scheduled Execution (SE)
    Preparation for layered Standards
Notes: Show co-sim and intermediate output notebooks

## Slide 27
Example model for hands-on part

## Slide 28: Example model: Controlled Motor Drive
Motor Drive with PI control modelled in Modelica
Load Step
at time 0,5s
Desired torque
Step at time 0,1s
Reference solution
Angular speed

## Slide 29: Example model: Controlled Motor Drive
Model exported as one overall FMU or split as three FMUs.
Load Step
at time 0,5s
Desired torque
Step at time 0,1s
Drive FMU
Control FMU
Stimuli FMU
Overall FMU

## Slide 30: Demo: FMU Export and import
FMU Export from Modelica-tool Dymola:
Configure options
FMU Import and Simulionat in Dymola: